## Slide 1: Data Logger For Mechanical Systems
Group 2:
Abdulrahman Al-Malki
Faisal Al-Mutawa
Mohammed Alsooj
Yasmin Hussein

## Slide 2: Outline
Project overview: Abdulrahman
Programming: Faisal
Components: Yasmin
PCB Design and Progress: Yasmin/Mohammed
Progress and Conclusion: Mohammed

## Slide 3: Project Overview
Same objective…
Dumb tool
Smart tool
+our product
Citations 1-2

## Slide 4: Project Overview
Different Execution
Citations 3-5

## Slide 5: Market Analysis – Customer Needs
Two personal interviews and one phone interview
Focus on:
  Vibration and rotation
  Prioritize accuracy
Figure 1

## Slide 6: Market Analysis - Benchmarking
Metric | Our Design Project | H.E.A.T Evaluation Module
Power Source | Lithium Battery | 3.3 V External Supply
Dimensions (LxWxH) | 5x1x1 inches | 15.6x1x0.93 inches
Sensors | Rotation and vibration | Rotation, pressure, temperature
Memory | 64 KB | 32 MB
Acquisition Frequency | 20 Hz | Up to 128k Hz
Connectivity | USB | CAN
Table 1: Comparison between our project and an existing product
Citations 6

## Slide 7: Top-level Model
Software: Abdulrahman and Faisal
Hardware: Mohammed and Yasmin
Our Project
Motion
Figure 2

## Slide 8: Programming – Flow Chart
Start
Initialize
Read ADC Data
Perform Calculations
Over threshold?
Yes
No
Figure 3
Store in Memory
Time<x?
Read ADC Data
Perform Calculations
True
False

## Slide 9: Programming – Call Graph
main()
Initialize_ADC()
Initialize_RTC()
SendUART()
Store()
ReadADC()
ReceiveUART()
LED()
Buttons()
CalculateADC()
Delay()
Mode()
Figure 4

## Slide 10: Programming – Functions
Function | Description
Main(); | Calls top-level functions
Initialize_RTC(); Initialize_ADC(); | Initialization for time & inputs
ReadADC(); | Read 3-analogue data inputs from sensor
SendUART(); ReceiveUART(); | Send data via RS-232 serial com.
Mode(); | Select mode or trigger of Data Acquisition
CalculateADC(); | Perform calculations of ADC Data
Store(); | Store calculated outputs in memory with a timestamp
Table 2: Details about the functions used in our project

## Slide 11: Programming - Modes
Mode | Description
00 | Continuous logging/stops when memory is full
01 | Starts logging after certain trigger for a certain period
1x | Continuous low frequency logging with triggers increasing the sampling rate
Table 2: Brief overview of the different modes of our project

## Slide 12: Main Components
Terminal Blocks
Crystal Oscillators
Push button Switches
LED
Chip (MAX323CD)
Connector
Capacitors
Resistors

## Slide 13: Schematics – Progress Report
Components Schematic | Status
LED indicators | Completed
ICD2 connector | Completed
Push Button Switches | Completed
Power Supply | Completed
Processor | Completed
Oscillators | Completed
Accelerometer | Pending…

## Slide 14: Schematic

## Slide 15: Schematics – Serial port

## Slide 16: Schematics – Push Buttons

## Slide 17: Schematics - Connector

## Slide 18: Schematics – LED

## Slide 19: References
http://m.c.lnkd.licdn.com/
http://www.logwell.com/capabilities/
http://www.solidworks.com/
http://www.yourcablestore.com/assets/
http://76.my/Malaysia/high-quality-usb-2-0-to-rs232-9-pin-serial-cable-1-5m-chocobozz
http://www.ti.com/tool/heatevm
http://www.mouser.com/

## Slide 20: Thank you for listening!
Any Questions?